## Slide 1
AM263X block diagram:

## Slide 2
OS
Kernel
Driver Porting Layer (DPL)
SOC Peripheral Drivers
No RTOS
FreeRTOS Kernel
FreeRTOS POSIX
Examples
Mbed TLS
Protocol stacks
And Middleware
Drivers and
HAL
Board Peripheral Drivers
Examples
And Demos
Tools
SysConfig
Code Composer Studio (CCS)
TI CLANG Compiler
TI Resource Explorer (TIREX)
ARM R5F, ARM M4F + SOC peripherals + EVM peripherals
X86 Host (Windows / Linux)
Demos
SDK Tools (Flashing, Boot, …)
LwIP (TCP/UDP)
Smart Placement
FreeRTOS + FAT

## Slide 3
AM64X/AM243X block diagram:

## Slide 4
OS
Kernel
Driver Porting Layer (DPL)
SOC Peripheral Drivers
No RTOS
FreeRTOS Kernel
FreeRTOS POSIX
Examples
Mbed TLS
Protocol stacks
And Middleware
Drivers and
HAL
Board Peripheral Drivers
Examples
And Demos
Tools
SysConfig
Code Composer Studio (CCS)
TI CLANG Compiler
TI Resource Explorer (TIREX)
ARM A53, ARM R5F, ARM M4F + SOC peripherals + EVM peripherals
X86 Host (Windows / Linux)
Demos
SDK Tools (Flashing, Boot, …)
LwIP (TCP/UDP)
TinyUSB
FreeRTOS + FAT

## Slide 5
OS
Kernel
Driver Porting Layer (DPL)
SOC Peripheral Drivers
No RTOS
FreeRTOS Kernel
FreeRTOS POSIX
Examples
Mbed TLS
Protocol stacks
And Middleware
Drivers and
HAL
Board Peripheral Drivers
Examples
And Demos
Tools
SysConfig
Code Composer Studio (CCS)
TI CLANG Compiler
TI Resource Explorer (TIREX)
ARM R5F, ARM M4F + SOC peripherals + EVM peripherals
X86 Host (Windows / Linux)
Demos
SDK Tools (Flashing, Boot, …)
LwIP (TCP/UDP)
Smart Placement
TinyUSB
FreeRTOS + FAT

## Slide 6
OS
Kernel
Driver Porting Layer (DPL)
SOC Peripheral Drivers
No RTOS
FreeRTOS Kernel
FreeRTOS POSIX
Examples
LwIP (TCP/UDP)
Protocol stacks
And Middleware
MMWave Framework
Drivers and
HAL
Board Peripheral Drivers
Examples
And Demos
Tools
SysConfig
Code Composer Studio (CCS)
TI CLANG Compiler
TI Resource Explorer (TIREX)
ARM R5F, TI C66x + SOC peripherals + EVM peripherals
X86 Host (Windows / Linux)
MMWave Demos
SDK Tools (Flashing, Boot, …)
TI C6000 Compiler

## Slide 7
7
Power switch
UART to USB
JTAG XDS110
BOOT MODE 0-15
Power supply (12V, 5A)
SD card

## Slide 8
8
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
NO BOOT MODE
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
UART BOOT MODE
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
OSPI BOOT MODE
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
SD BOOT MODE

## Slide 9
9
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
EMMC BOOT MODE
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
DEV BOOT MODE
BOOTMODE
0:7 (SW2)
BOOTMODE
8:15 (SW3)
PCIE BOOT MODE

## Slide 10
10
UART to USB
JTAG XDS110
BOOT MODE SW3 (0-7)
Power supply (5V, 3A)
BOOT MODE SW2 (8-15)

## Slide 11
11
c
c
BOOTMODE
0:7 (SW3)
BOOTMODE
8:15 (SW2)
UART BOOT MODE
c
c
BOOTMODE
0:7 (SW3)
BOOTMODE
8:15 (SW2)
OSPI BOOT MODE

## Slide 12
12
c
c
BOOTMODE
0:7 (SW3)
BOOTMODE
8:15 (SW2)
SD BOOT MODE
c
c
BOOTMODE
0:7 (SW3)
BOOTMODE
8:15 (SW2)
NO BOOT MODE

## Slide 13
13
c
c
BOOTMODE
0:7 (SW3)
BOOTMODE
8:15 (SW2)
EMMC BOOT MODE

## Slide 14
Power Supply
(12V 5A)
Jtag XDS 110
Uart to USB
Boot Mode
Switches
Reset Button

## Slide 15
15
Power Supply
(12V 5A)
Jtag XDS 110
Uart to USB
Boot Mode
Switches
Reset Button

## Slide 16
Application
Layer 1 - Physical
Layer 2 - Data Link
Layer 7 - Application
TI
Customer
Third Party
PRU Firmware
PRUICSS with 2x MII
PRUICSS Driver
FW HAL for EtherCAT Slave
EtherCAT Slave Stack
ARM
Processor
PRUICSS
Ethernet PHY
Ethernet PHY

## Slide 17
RPRC Format
RPRC Header
Section 1 Header
Section 1 Content
Section 2 Header
Section 2 Content
Section 3 Header
Section 3 Content
RPRC Magic Word
Entry Point
Reserved
Section Count
Version
Section Run Address
Reserved
Section Size
Reserved
Reserved
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
Offset
(20 Bytes)
(20 Bytes)

## Slide 18
RPRC Format
RPRC Header
Section 1 Header
Section 1 Content
Section 2 Header
Section 2 Content
Section 3 Header
Section 3 Content
RPRC Magic Word
Entry Point
Reserved
Section Count
Version
Section Run Address
Reserved
Section Size
Reserved
Reserved
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
Offset
(20 Bytes)
(20 Bytes)

## Slide 19
XIP gen
19
RPRC Header (entry point = 0x0)
Section 1 Header (addr = 0x0, size = 0x80)
Section 1 Content
Section 2 Header (addr = 0x70080000, size = 8KB)
Section 2 Content
Section 3 Header (addr = 0x60100000, size = 64KB)
Section 3 Content
Section 4 Header (addr = 0x60110000, size = 16KB)
Section 4 Content
xipGen
RPRC Header (entry point = 0x0)
Section 1 Header (addr = 0x0, size = 0x80)
Section 1 Content
Section 2 Header (addr = 0x70080000, size = 8KB)
Section 2 Content
RPRC Header (entry point = NOT USED)
Section 1 Header (addr = 0x60100000, size = 80 KB)
Section 1 Content (merged content of section 3 + section 4)
Non-XIP RPRC file
XIP RPRC file
XIP sections
Merged
XIP section

## Slide 20
…
v
Post build steps
20
.c
.c
.obj
.obj
.lib
.out
…
…
.rprc
.rprc
.rprc_xip
compiler
linker
compiler
out2rpc
xipGen
CPU1
v
.c
.c
.obj
.obj
.lib
.out
…
…
.rprc
.rprc
.rprc_xip
compiler
linker
compiler
out2rpc
xipGen
CPUn
.appimage
.appimage_xip
multiCoreGen
multiCoreGen

## Slide 21
…
v
Post build steps
21
.c
.c
.obj
.obj
.lib
.out
…
…
.rprc
compiler
linker
compiler
out2rpc
CPU1
v
.c
.c
.obj
.obj
.lib
.out
…
…
.rprc
compiler
linker
compiler
out2rpc
CPUn
.appimage
multiCoreGen

## Slide 22
Multi-core Image
Multi-Core Header
Core 1 Meta Header
Core 2 Meta Header
….
Header End
Core 1 RPRC
Core 2 RPRC
….
Core N RPRC
Magic Word
Number of Cores
Device ID
Reserved
Core ID
RPPC Image Offset
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000000
0x00000004
Offset
(16 Bytes)
(8 Bytes)
Reserved
End of Header
0x00000000
0x00000004
(8 Bytes)
Meta Header
RPRC Images
*Refer RPRC Format
Offset: 0x10 + (8 * Core Index)
Offset: 0x10 + (8 * Num Cores)

## Slide 23
R5F application
User Space application
Kernel Space
23
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-0
RP Message
RP Message Char
User Application
Linux Kernel
A53
User Application
R5F application
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-1
User Application
Mail Box Driver
M4F application
IPC Notify
NO RTOS or FreeRTOS
M4FSS0-0
User Application
IPC RP Message

## Slide 24
R5F application
24
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-0
User Application
R5F application
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-1
User Application
R5F application
IPC Notify
NO RTOS or FreeRTOS
R5FSS1-0
User Application
IPC RP Message
R5F application
IPC Notify
NO RTOS or FreeRTOS
R5FSS1-1
User Application
IPC RP Message

## Slide 25
R5F application
25
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-0
User Application
R5F application
IPC Notify
IPC RP Message
NO RTOS or FreeRTOS
R5FSS0-1
User Application
C66 application
IPC Notify
NO RTOS or FreeRTOS
C66 DSP
User Application
IPC RP Message

## Slide 26
26
Enable IPC between current CPU and another CPU
Keep IPC disabled with a CPU if not needed
Check this to enable IPC with Linux

## Slide 27
27
Enable IPC between current CPU and another CPU

## Slide 28
28
Enable IPC between current CPU and another CPU

## Slide 29
Boot flow
29
ROM Bootloader (RBL)
POWER-ON
Secondary Bootloader (SBL)
Application Binary
ROM BOOT
SBL BOOT

## Slide 30
SBL Boot flow
30
MULTICORE APPIMAGE
SBL Parse
RPRC 1
…….
…….
RPRC N
RPRCs for N CPUs were found in the multicore appimage
For each RPRC
Initialize Core
Load RPRC Image
Set Entry Point
Release Core from Reset

## Slide 31
Device Driver
SOC Specific USB Controller Hardware
Tiny USB
USB Device Core Driver
SoC Porting Layer
Application Layer
TinyUSB Porting Layer (DCD)
FreeRTOS / NORTOS Services
CDC-ACM Class
cdc_echo example
USB Device Core

## Slide 32
Application
Layer 1 - Physical
Layer 2 - Data Link
Layer 7 - Application
PRU Firmware
PRUICSS with 2x MII/RGMII
PRUICSS Driver
EtherNet/IP Adapter FWHAL
EtherNet/IP Adapter Stack
ARM
Processor
PRUICSS
Ethernet PHY
Ethernet PHY
ICSS-EMAC
lwIP Stack
TI
Customer
TI / Third Party

## Slide 33
33
ARM
L3 RAM
If PTP/DLR ?
PTP Driver+Stack/DLR Driver
TCP/IP Stack
Priority Queue 0
Priority Queue 1
Priority Queue 2
Priority Queue 3
Yes
No

## Slide 34
Application
Layer 1 - Physical
Layer 2 - Data Link
Layer 7 - Application
PRU Firmware
PRUICSS with 2x MII/RGMII
PRUICSS Driver
Profinet Device FWHAL
Profinet Device Stack
ARM
Processor
PRUICSS
Ethernet PHY
Ethernet PHY
ICSS-EMAC
lwIP Stack (including SNMP)
TI
Customer
TI / Third Party

## Slide 35
Application
Layer 1 - Physical
Layer 2 - Data Link
Layer 7 - Application
PRU Firmware
PRUICSS with 2x MII/RGMII
PRUICSS Driver
PRP FWHAL
ARM
Processor
PRUICSS
Ethernet PHY
Ethernet PHY
ICSS-EMAC
lwIP Stack (including SNMP)

## Slide 36
36
ARM
MSRAM
Profinet Stack
lwIP Stack
Priority Queue 0
Priority Queue 1
Priority Queue 2
Priority Queue 3
LLDP, MRP, PTCP
RTA, DCP
VLAN Priority
4-7
VLAN Priority
0-3

## Slide 37
HOST
Queue 1
Queue 2
Queue 3
Queue 4
Collision Queue
PORT 0
Queue 1
Queue 2
Queue 3
Queue 4
Collision Queue
PORT 1
Queue 1
Queue 2
Queue 3
Queue 4
Collision Queue

## Slide 38
MII/RGMII picks up the data and copies it to L2 FIFO and sends a signal to firmware
Firmware copies the data to queue buffers (MSRAM) and signals host through an interrupt
Host services the interrupt and copies the data from MSRAM to application buffers
Application creates the packet
Host copies the data to queue buffers (MSRAM) from application buffers and signals PRU to pick it up
Firmware picks up the data and puts it in Tx FIFO
MII/RGMII picks up the data and sends it on the wire
ICSS EMAC RX/TX Data Path
RX
TX

## Slide 39
ICSS EMAC Storm Prevention Architecture
39
Broadcast/
Multicast Packet Received
Storm Prevention Credits
Drop Packet
Decrement Credits
Allow packet to pass
Check Credit Value
On PRU
Credits = 0
Credit Value > 0
Reset value with default
On ARM

## Slide 40
40
EVM
192.168.1.100
HOST PC
192.168.1.101
ROUTER with
DHCP SERVER
192.168.1.1

## Slide 41
41

## Slide 42
42
EPWM 0
ADC 2
ADC 1
SOC A
SOC0
SOC1
SOC2
SOC2
SOC1
SOC0
RESULT0
RESULT1
RESULT2
RESULT0
RESULT1
RESULT2
AM263 - ADC Multiple SOC EPWM Example

## Slide 43
43
EPWM 0
ADC 2
SOC A
SOC0
SOC1
SOC12
RESULT0
RESULT1
RESULT2
AM263 - ADC Burst Mode Oversampling Example
SOC13
SOC14
SOC15
Burst mode enabled

## Slide 44
44
EPWM 0
ADC 2
ADC 1
SOC A
SOC0
SOC0
RESULT0
RESULT0
DMA Channel 0
DMA Channel 1
RESULT BUFFER0
RESULT BUFFER1
AM263 - ADC SOC Continuous DMA Example

## Slide 45
45
RTI1
EDMA
DAC
AM263 – DAC DMA Sine wave Example
DMA Trigger
Sine Table
(Buffer with sine values)
Sine wave output
EDMA Source
EDMA Destination

## Slide 46
46
EPWM
Counter Compare
Time Base
DMA XBar
DMA Trigger XBar
EDMA
SOCA
Configuration Array
Data transfer to EPWM registers

## Slide 47
47
CMPSSA
EPWM
CTRIPOUTH
PWM_B
CMPINxP
OUTPUT XBAR
XBAROUT
TRIP4
CTRIPH
PWM output signal
CMPSS input signal
Internal DAC output
t
t
CMPIN1P exceeds internal DAC output
PWM tripped
Input signal to CMPSS
PWM output signal
Trip output signal

## Slide 48
48
PWM output signal
DAC Output signal
(ADC Input)
PPB High level
t
t
ADC Input exceeds PPB High limit
PWM tripped
DAC
Ramp Waveform
ADC
PPB
ADC EVT
EPWM0
OST TRIP Input
PWM output signal
PPB Low level
EPWM1
CBC TRIP Input
PWM output signal
EPWM2
Direct TRIP Input
PWM output signal
ADC EVT
ADC EVT

## Slide 49
49

## Slide 50
50
EPWM(0-4)
EPMWA
EPMWB
HRPWM Micro-edge Positioner (MEP) Calibration Module
HRMSTEP
HRCNFG
CMPAHR(8)
CMPBHR(8)
TBPRDHR(8)
ePWMxA
ePWMxB

## Slide 51
SCICLIENT OPERATION
51
APPLICATION
SCICLIENT
Any system control request – resource, power, clock, security
Sciclient sends a TISCI message to the SYSFW/HSM Runtime with the specifics of the request, on a secure proxy thread allotted for this particular core.
SYSFW/HSM Runtime
SECURE PROXY THREAD
SYSFW sends back a response after processing the request

## Slide 52
52
SCICLIENT
RESOURCE MANAGEMENT
POWER MANAGEMENT
SECURITY
FIREWALLS
PROCESSOR BOOT

## Slide 53
53
SYSFW-HS-FS
SYSFW-HS-FS-ENC
TI MEK
Unsigned, unencrypted SYSFW for HS-FS device
Encrypted SYSFW for HS-FS device
(sysfw-hs-fs-enc.bin)
TI MPK
SYSFW-HS-FS-ENC-CERT
X509 Certificate for the Encrypted SYSFW for HS-FS device
(sysfw-hs-fs-enc-cert.bin)
SYSFW
Unsigned, unencrypted SYSFW for GP device
(sysfw.bin)

## Slide 54
54
SBL image
X509 Certificate
SBL image
x509 Certificate
SYSFW
Board Config

## Slide 55
55
Device Type | Validation Requirements for SBL |  |  | Validation Requirements for HSMRt/SYSFW |  | 
 | Certificate Verification | Image Integrity Protection | Image Decryption | Certificate Verification | Image Integrity Protection | Image Decryption
HS-FS | Not Performed | Optional | Not Performed | Required | Required | Optional
HS-SE | Required | Required | Optional | Required | Required | Optional
GP | Not Performed | Optional | Not Performed | Not Performed (N/A in case of HSMRt) | Not Performed (N/A in case of HSMRt) | Not Performed (N/A in case of HSMRt)

## Slide 56
Target EVM
(Running SBL PCIE)
Target EVM
(Running SBL PCIE HOST)
Initialize PCIe
Initialize PCIe
Configure ATU for receiving appimage
Notify host application ready to receive appimage
Transfer SBL PCIe image
Transfer application image
Notify target EVM offset to which image is send
Mark image transfer completion with “MAGIC WORD”
Authenticate and boot application on receiving the “MAGIC WORD”
Skipped if booting in PCIe boot mode. Use ROM configuration for PCIe instead
Initialization and link training will happen with ROM if target boots in PCIe boot mode. Else link training happens with SBL PCIE
Happens only if target EVM is booting in PCIe boot mode.
Wait for notification from target EVM